### Canon de 220  L  Mle  1917  Schneider

## Manufacturer:			Schneider et Cie., Le Creusot, France

Calibre				220mm

Length of barrel			L/35 (L34.87):  7,672.5mm

## Length of rifling 		(L/26.80): 6,113.5mm

Twist of rifling			92 grooves, 7 degrees (to right)

Barrel construction		Jacketed

Weights			Barrel – 9,280kg (with breech block)

Weight travelling		(1 load): 25,880kg; (2 loads): 30,120kg

#### Weight in action		23,000kg

Traverse			360 degrees

Elevation			0 to +37 degrees

Ammunition			22cm Gr. 534 (f)  weight:       104.05kg

M/velocity 754m/sec

Range :       21,600m

22cm Gr. 535 (f) weight:        104.75kg

M/velocity  766m/sec

Range:         22,800m

Charge weight			20kg

Rate of fire			1 round/minute

Guernsey Armouries

### BATTERIE  GENERALOBERST

###### DOLLMANN

No. 3 GUN  PIT

SOUVENIR GUIDE

# BATTERIE

GENERALOBERST  DOLLMANN

Following Hitler’s directive of October 1941, that the Channel Islands should be turned into a naval fortress, it was soon apparent that the navy alone would be unable to fulfill all its commitments and so as a temporary measure, the army was called upon to help bring the coastal artillery up to strength. However the replacement navy weapons never arrived  and the army batteries remained operational up until liberation in 1945.

Batterie Generaloberst Dollmann was manned by the 15th Battery of the IV Battalion of the 1265 Artillery Regiment and was operational by December 1941.

The Batterie was equipped with 4 x 22cm K532(f) guns, which had a range of 22 kilometres, housed in separate pits and controlled via the Lietstand (command centre) visible adjacent to the car park at the end of this headland.

Guernsey Armouries

Sans Souci, Le Villocq, Castel, GY5 7SA

Tel. 253792

Ian Brehaut

Tony Froome

David Malledent

MICK LANYON

THE RECOVERY AND RESTORATION

Following the recovery by Guernsey Armouries of a 22cm

K532(f) barrel from Jersey in 1995, this position was selected

to be restored as an example of a German heavy coastal artillery batterie.  After removing 1,000 tons of backfill from the site, a chassis and mount were fabricated using copies of the original blueprints obtained from the French Ministry of Defence (namely the Centre d’Archives de l’Armament in Chatellerault.) The gun was positioned in the restored emplacement in June 2001.

The guns were originally cannon de 220L MLE 1917 Schneider

manufactured during WW1 for the French Army. When in 1940 the

German Army overran France they were captured and later re-deployed

for coastal defence. After liberation in 1945, the guns remained in position until scrapped and the emplacements backfilled and landscaped in 1948.